## Slide 1
• PROJECT EXPO
DESIGN & SIMULATION OF A
DIGITAL ERROR DETECTION SYSTEM
USING PARITY
TRANSMIT → CHECK → DETECT
SECTION - 6
Team Members: Likhita 2620030468
Dheeraj 2620030472
Rupesh 2620030517
Druveen 2620030528.]
Parity detects many transmission errors — but does not correct them.

## Slide 2
PARITY LAB / DIGITAL LOGIC DESIGN EXPO PROJECT • 02/06
Why parity-based error detection?
A simple extra bit helps a receiver detect whether a data word may have changed in transit.
THE PROBLEM
Digital data can be corrupted by noise, interference, or faults during storage and transmission.
THE IDEA
Append one parity bit so the total number of 1s is even (even parity) or odd (odd parity).
THE OBJECTIVE
Build and simulate a logic circuit that checks parity and raises an error flag when parity is invalid.
PROJECT OBJECTIVES
01
Generate / use a parity bit for a data word.
02
Recompute parity at the receiver using XOR gates.
03
Compare received parity with the expected parity.
04
Validate normal and corrupted cases in Logisim.
SCOPE
Single-bit parity check
Detects odd-number bit flips; may miss even-number flips.
DESIGN • SIMULATE • VERIFY
2/6

## Slide 3
PARITY LAB / DIGITAL LOGIC DESIGN EXPO PROJECT • 03/06
Theory & logic circuit
Even-parity checker for a received 4-bit data word D3 D2 D1 D0 and parity bit P.
XOR PROPERTY
A ⊕ B = 1 when inputs differ; 0 when they match.
EVEN PARITY
Valid codeword has an even number of 1s: D3 ⊕ D2 ⊕ D1 ⊕ D0 ⊕ P = 0.
ERROR FLAG
E = D3 ⊕ D2 ⊕ D1 ⊕ D0 ⊕ P
E=0: parity OK • E=1: error detected
5-INPUT XOR CHECKER
D3
D2
D1
D0
P
⊕
⊕
⊕
⊕
⊕
E = D3 ⊕ D2 ⊕ D1 ⊕ D0 ⊕ P
Use cascaded XOR gates (or a 5-input XOR equivalent). If the result is 1, the received word has odd parity.
DESIGN • SIMULATE • VERIFY
3/6

## Slide 4
PARITY LAB / DIGITAL LOGIC DESIGN EXPO PROJECT • 04/06
Circuit design in Logisim
Implementation plan: use input pins, XOR gates, and an output indicator.
5 input pins: D3, D2, D1, D0, P
4 XOR gates cascaded into one final result (5-input parity).
2 CONNECT THE LOGIC
Chain XOR outputs into the next XOR input; connect the final output to E.
3 TEST THE CIRCUIT
Toggle inputs with the poke tool. Check E against the expected parity.
Circuit Design in Logisim
LOGISIM-STYLE CIRCUIT SCHEMATIC • CONCEPTUAL
D3
D2
D1
D0
P
⊕
⊕
⊕
⊕
E FLAG
E = XOR of all 5 received bits
DESIGN • SIMULATE • VERIFY
4/6
1 PLACE COMPONENTS

## Slide 5
PARITY LAB / DIGITAL LOGIC DESIGN EXPO PROJECT • 05/06
Simulation results & truth table
Expected behavior for an even-parity checker: E=0 when total 1s are even; E=1 when odd.
TEST VECTORS (REPRESENTATIVE)
D3 D2 D1 D0 P
Total 1s
E
Interpretation
0 0 0 0 0
0
0
Valid
0 0 0 0 1
1
1
Error
0 0 0 1 1
2
0
Valid
1 0 1 0 0
2
0
Valid
1 0 1 0 1
3
1
Error
1 1 1 1 0
4
0
Valid
1 1 1 1 1
5
1
Error
CASE A • VALID
Received bits: 1 0 1 0 1 → total 1s = 3 → E=1 (error detected)
CASE A • VALID
Received bits: 1 0 1 0 0 → two 1s → E = 0
CASE B • ERROR DETECTED
Received bits: 1 0 1 0 1 → three 1s → E = 1
DESIGN • SIMULATE • VERIFY
5/6

## Slide 6
PARITY LAB / DIGITAL LOGIC DESIGN EXPO PROJECT • 06/06
Conclusion, applications & next steps
A lightweight hardware check that demonstrates parity generation, XOR logic, and simulation-based verification.
CONCLUSION
The XOR checker correctly flags received words with odd parity and accepts words with even parity.
APPLICATIONS
Serial links, memory checks, simple communication protocols, digital systems labs, and introductory fault detection.
LIMITATIONS
Parity detects any odd number of bit flips, but can miss an even number of bit flips; it cannot locate or correct an error.
FUTURE IMPROVEMENTS
+
Add a parity generator at the transmitter and a checker at the receiver.
+
Display PASS / ERROR with LEDs and add switch-based test vectors.
+
Extend to two-dimensional parity or use a Hamming code for error correction.
THANK YOU
DESIGN • SIMULATE • VERIFY
6/6